- FlatCam needs filled poygons in order to do edge cuts properly.
  Kicad doesn't create filled polygons.
  So I created a script which converts lines into a filled polygon

  fill-edge-cuts.py Nanino8-Edge.Cuts.gbr

  This generates Nanino8-Edge.Cuts-filled.gbr

- In pcbNew
- Set the grid origin (Place->Grid Origin) and click in bottom left of arduino board
- Set Drill and Place Offset (aka aux axis) to bottom left corner of board
- This sets the origin for the gerber/gcode files.
- When plotting gerbers, check "Use auxilliary axis as origin"
- When making drill files. Set Drill Origin to "Auxilliary axis"
- In gerber viewer, confirm origin location
- For http://dangerousprototypes.com/store/pcbs Check "Use Protel file extensions"
 and the rename-gerbers.py script.

- python flatcam.py
- Import gerbers
Nanino8-B.Cu.gbr
Nanino8-Edge.Cuts-filled.gbr
- Import Excellon
Nanino8.drl
Nanino8-NPTH.drl

- Double click on Nanino8-Edge.Cuts-filled.gbr
- Board cutout only cuts out rectangular
- so we use isolation routing with a larger endmill 3.125 mm (1/8")
- generate geometry

- Add Tabs
- click on the "Projects" tab
- Click once on the Nanino8-B-Edge-Cuts-filled.gbr_iso geometry
- Edit->Edit-Geometry
- Click on rectangle and draw out tabs
- Click-Drag and then click again when done
- Want tabs about 2 endmill widths wide
- Press ESC (should highlight the Arrow)
- Click on the outline and Control-Click the tabs in that order
- Drawing->Cut-Path
- Press ESC
- Click on first tab and control-Click on the rest of the tabs
- Drawing->Delete Shape
- Edit->Update Geometry
- Should now have a path with some gaps in it

- Double click on Nanino8-B.Cu.gbr
- 0.48mm (0.019")
- generate geometry
- Double click on Nanino8-NPTH.drl
- Mill Holes - 3.125mm
- Double click on Nanino8.drl
- Can either drill or mill
- to mill pick a small mill (smaller than the smallest hole)
- generate geometry
- to drill
- pick Cut Z -2mm
- Travel Z 3 mm
- Feed rate 75 mm/min
- Double click on Nanino8-NPTH.drl_mill
CutZ -2 mm
TravelZ 3 mm
Feed Rate 150 mm/min
Tool dia: 3.125mm
- Generate
- Double click on Nanino8-B.Cu.gbr_iso
CutX .15 mm
TravelZ 3 mm
Feed Rate: 380 mm/min
Tool Dia: 0.5 mm
- Generate
- Double click on Nanino8-B-Edge-Cuts-filled.gbr_iso
CutZ -2 mm
TravelZ 3 mm
Feed Rate 150 mm/min
Tool dia: 3.125mm
- Generate

Not verified!
Isolation feed rate 15 IPM = 380 mm/min
Edge cut feed rate 6 IPM = 150 mm/min